## Slide 1: RegTrack
Relative GPS Tracking
Institute for Software
Integrated Systems
Vanderbilt University
Akos Ledeczi
Peter Volgyesi
Will Hedgecock
Miklos Maroti
Janos Sallai
“High-Accuracy Differential Tracking of Low-Cost GPS Receivers”

## Slide 2: Outline
Motivation
Requirements and Overview
Technical Methodology
Experimental Implementation
Results (Demo)
Conclusions and Future Work

## Slide 3: Motivation
Many WSN applications rely on highly-accurate sensor node locations in which ONLY the relative positions of the nodes are required
GPS provides absolute coordinates anywhere in the world, but sub-meter accuracy is unobtainable without military-grade or prohibitively-expensive differential GPS units
Precision Agriculture
Land Surveying
Autonomous Driving
Formation Flying

## Slide 4: Requirements
Centimeter-precision accuracy for a scalable network of nodes
No stationary calibration or data collection phase
No explicit reference station or hub
Our Approach
Use GPS satellites to provide centimeter-scale relative position accuracy in a cooperating network of sensor nodes via raw data sharing and pairwise node localization

## Slide 6: Methodology
Three-fold Approach
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Extend well-known observation models to include between-epoch data without requiring a reference satellite
    Temporal double-difference
    Dual-epoch, double-difference
Use the new observation model in a GPS tracking algorithm to enable robust relative dead reckoning through a significant period of time

## Slide 7
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
Known Errors:
  Satellite and receiver clock biases
  Atmospheric signal delays
  Antenna phase center offsets
  Satellite orbital errors
  Multipath
  Carrier wave cycle slips

## Slide 8
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
  Significant uncharacterized error in the geometrical differences arising from measurements taken at slightly different times:
  Range errors in the satellite observations due to physically different signal propagation path lengths
  Inconsistent satellite orbital position estimations
  Differing amounts of Earth rotation experienced during potentially different signal propagation times

## Slide 9
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
  Solved via full extrapolation of observation data to a common receive epoch and updating the satellite positions to the locations at which they must have been when transmitting the corresponding signal that would have been received at the common epoch

## Slide 10
Technique
Approach Step #1

## Slide 11
Technique
Approach Step #1

## Slide 12
Technique
Approach Step #1

## Slide 13
Technique
Approach Step #1

## Slide 14
Technique
Approach Step #1

## Slide 15
Technique
Approach Step #1

## Slide 16
Technique
Approach Step #1

## Slide 17
Technique
Approach Step #1

## Slide 18
Extend well-known observation model to include between-epoch data without requiring a reference satellite
Technique
Approach Step #2

## Slide 19
Use the temporal double-differenced observations in a GPS tracking equation to enable robust relative dead reckoning through a significant period of time
Technique
Approach Step #3
= 0 =

## Slide 20
Implementation

## Slide 21
Results

## Slide 22
Results

## Slide 23
Results

## Slide 24
Results from tracking algorithm will allow for baseline calculation to collapse to the stationary case
Multiple epochs of data will provide much needed GPS satellite constellation changes for the removal of unlikely ambiguity sets
This combination should enable rapid on-the-fly (OTF) ambiguity resolution, as well as verification
Future Work
Extension of successful methodology to include cooperative network adjustments for both increased precision and faster ambiguity resolution
We only solved half of the problem
Initial baseline determination and re-initialization upon loss of satellite locks

## Slide 25: Questions?
Institute for Software
Integrated Systems
Vanderbilt University
Akos Ledeczi
Peter Volgyesi
Will Hedgecock
Miklos Maroti
Janos Sallai
“High-Accuracy Differential Tracking of Low-Cost GPS Receivers”

## Slide 26
Results

## Slide 27
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
  Full extrapolation of observation data to a common receive epoch:
Estimate receiver clock bias using simple least squares optimization
Calculate satellite-receiver range at actual time of transmission/reception:
Determine satellite range change during receiver bias from system time:
Update observations with this change in range
Iteratively solve for the transmission time of the signal that would have been received exactly at the epoch: