## Slide 1: High-Precision Relative Positioning with GPS
Institute for Software
Integrated Systems
Vanderbilt University
Will Hedgecock
WithIT Seminar, September 26, 2013

## Slide 2: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 3: Motivation
Many WSN applications rely on highly-accurate sensor node locations in which ONLY the relative positions of the nodes are required
GPS provides absolute coordinates anywhere in the world, but sub-meter accuracy is unobtainable without military-grade or prohibitively-expensive differential GPS units
Precision Agriculture
Land Surveying
Autonomous Driving
Formation Flying

## Slide 4: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 5: Requirements
Centimeter-precision accuracy for a scalable network of nodes
No stationary calibration or data collection phase
No explicit reference station or hub
Our Approach
Use GPS satellites to provide centimeter-scale relative position accuracy in a cooperating network of sensor nodes via raw data sharing and pairwise node localization

## Slide 7: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 8: Observables and Terminology
Pseudorange
  Time-of-flight (TOF)-based measurement observable

## Slide 9: Observables and Terminology
Doppler Shift

## Slide 10: Observables and Terminology
Carrier Phase

## Slide 11: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 12: Related Work
Real-Time Kinematic (RTK) Navigation
“RTK uses measurements of the phase of the signal′s carrier wave, rather than the information content of the signal, and relies on a single reference station to provide real-time corrections, providing up to centimeter-level accuracy” --Wikipedia
“RTK uses measurements of the phase of the signal′s carrier wave, rather than the information content of the signal, and relies on a single reference station to provide real-time corrections, providing up to centimeter-level accuracy” --Wikipedia
“RTK uses measurements of the phase of the signal′s carrier wave, rather than the information content of the signal, and relies on a single reference station to provide real-time corrections, providing up to centimeter-level accuracy” --Wikipedia
Centimeter-precision accuracy for a scalable network of nodes
No stationary calibration or data collection phase
No explicit reference station or hub

## Slide 13: Methodology
Five-Step Approach
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Extend well-known observation models to include between-epoch data without requiring a reference satellite
Use the new observation models in a GPS tracking algorithm to enable robust relative dead reckoning through a significant period of time
Use the tracking results to mathematically reverse any relative receiver motions such that the observation models collapse to the stationary case
Combine multiple epochs of ‘collapsed’ satellite observations in an Ambiguity Function Method (AFM) algorithm to solve for relative baselines

## Slide 14
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
Known Errors:
  Satellite and receiver clock biases
  Atmospheric signal delays
  Antenna phase center offsets
  Satellite orbital errors
  Multipath
  Carrier wave cycle slips

## Slide 15
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
  Significant uncharacterized error in the geometrical differences arising from measurements taken at slightly different times:
  Range errors in the satellite observations due to physically different signal propagation path lengths
  Inconsistent satellite orbital position estimations
  Differing amounts of Earth rotation experienced during potentially different signal propagation times

## Slide 16
Characterize and correct for previously unexplored or ignored sources of error specific to the two-receiver localization case
Technique
Approach Step #1
  Solved via full extrapolation of observation data to a common receive epoch and updating the satellite positions to the locations at which they must have been when transmitting the corresponding signal that would have been received at the common epoch

## Slide 17
Technique
Approach Step #1

## Slide 18
Technique
Approach Step #1

## Slide 19
Technique
Approach Step #1

## Slide 20
Technique
Approach Step #1

## Slide 21
Technique
Approach Step #1

## Slide 22
Technique
Approach Step #1

## Slide 23
Technique
Approach Step #1

## Slide 24
Technique
Approach Step #1
Hedgecock, W., M. Maroti, J. Sallai, P. Volgyesi, and A. Ledeczi, "High-Accuracy Differential Tracking of Low-Cost GPS Receivers", ACM 11th International Conference on Mobile Systems, Applications, and Services (MobiSys '13), Taipei, Taiwan, ACM, 06/2013.

## Slide 25
Extend well-known observation model to include between-epoch data without requiring a reference satellite
Technique
Approach Step #2

## Slide 26
Use the temporal double-differenced observations in a GPS tracking equation to enable robust relative dead reckoning through a significant period of time
Technique
Approach Step #3
= 0 =

## Slide 27
Use the tracking results to mathematically reverse any relative receiver motions such that the observation models collapse to the stationary case
Technique
Approach Step #4

## Slide 28
Combine multiple epochs of ‘collapsed’ satellite observations in an Ambiguity Function Method (AFM) algorithm to solve for relative baselines
Technique
Approach Step #5
At the correct position, the sum of the distances from the receiver to the nearest integer ambiguity will be minimized

## Slide 29
Combine multiple epochs of ‘collapsed’ satellite observations in an Ambiguity Function Method (AFM) algorithm to solve for relative baselines
Technique
Approach Step #5
*Modified from Dr. Mark Petovello’s ION GNSS 2013 Presentation: “RTK GNSS Positioning”

## Slide 30
Combine multiple epochs of ‘collapsed’ satellite observations in an Ambiguity Function Method (AFM) algorithm to solve for relative baselines
Technique
Approach Step #5
Known:
Therefore:

## Slide 31
Combine multiple epochs of ‘collapsed’ satellite observations in an Ambiguity Function Method (AFM) algorithm to solve for relative baselines
Technique
Approach Step #5
Immune to carrier phase cycle slips!

## Slide 32: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 33
Results from tracking algorithm will allow for baseline calculation to collapse to the stationary case
Multiple epochs of data will provide much needed GPS satellite constellation changes for the removal of unlikely ambiguity sets
This combination should enable rapid on-the-fly (OTF) ambiguity resolution, as well as verification
Future Work
Extension of successful methodology to include cooperative network adjustments for both increased precision and faster ambiguity resolution
We only solved half of the problem
Initial baseline determination and re-initialization upon loss of satellite locks

## Slide 34: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 35
Implementation
Hardware Architecture

## Slide 36
Implementation
Software Architecture
Distributed, Multi-Agent System
Software agent-based system comprising distinct, distributed agents running on physically separate devices and communicating over a network
“Software Agent”: A computer program whose purpose is to act on behalf of or provide a data resource for a standalone application
  Background service capable of providing localization services to a requesting application
“Multi-Agent”: The system comprises multiple distinct software agents to provide functionality
“Distributed”: The multiple agents are disseminated among separate and unique devices

## Slide 37
Implementation
Software Architecture

## Slide 38: Outline
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)
Motivation
Requirements and Overview
GPS Measurement Observables and Terminology
Technical Methodology
Future Work
Experimental Implementation
Results (Demo)

## Slide 39
Results

## Slide 40
Results

## Slide 41
Results

## Slide 42: Questions?
Institute for Software
Integrated Systems
Vanderbilt University
Will Hedgecock
WithIT Seminar, September 26, 2013